## Slide 1: Aaria model
Manual control with joystick

## Slide 2: Opening the model
Download the model folder: AariaR2017a
https://bit.ly/2zgyQzU
https://github.com/AariaRobot/Joystick-Control
Open MATLAB R2017a
Open files
  AariaJoystickR2017a.slx
  AariaUI2017a.m
AariaJoystickR2017a.slx will open in a new window
Run AariaUI2017a.m to open the User Interface

## Slide 5
Input desired DH-parameters using the modified notation
Values must be numeric pi = 3.142, pi/2 = 1.571
Set the link types: 1 = revolute joint, 2 = prismatic joint, 0 = empty
Click “Simulate” button to begin simulation
Click “Stop simulation” to stop the simulation

## Slide 6
Alternatively, you can simulate a preset manipulator model by clicking one the buttons in the bottom left
The simulation can be stopped by clicking the “Stop simulation” button

## Slide 7
The simulation visualization will appear in a new window or a tab in MATLAB
Zoom the view with scroll wheel
Rotate the view by dragging with middle mouse button
Cursor location matters

## Slide 8: Joystick controls
Joint 1: Left and Right
Joint 2: Front and Back
Joint 3: Twist Clockwise and Counterclockwise
Joint 4: Lever Up and Down
Joint 5: Buttons 3 and 4
Joint 6: Buttons 7 and 8
Grab: Trigger

## Slide 10: Plotting
0. plot(1,1) in command window
1. simOut in Workspace
2. SensorData
3. Paint columns and click
plot from the plots tab

## Slide 13
Select magnifying glass
Drag a box around the
part you want to zoom
Double click the graph
to return to normal view

## Slide 14: The data
SensorData table column guide:
1 time,
2-7 joint values[radians or meters]
8-13 base sensor, [xyz angular velocity, xyz acceleration]
14-19 tool sensor, [xyz angular velocity, xyz acceleration]
20-31 link 1 sensors [xyz angular velocity, xyz acceleration] X 2
32-43, 44-55, 56-67, 68-79, 80-91
each link to 91 when using 2 sensor for each link
This info is written in AariaParams12J.m file on line 35

## Slide 15
Try to grab the yellow box
The tool needs to be close enough and in the right orientation

## Slide 16: Good Luck!